## Slide 1
Coordinator ECRAN KE 2
Ike van der Putte
TASK 4: Compliance with REACH/CLP
TASK 5: Transfrontier Shipment of Waste

## Slide 2
TASK 4: Compliance with REACH/CLP

## Slide 3: A New EU Chemicals Policy
Registration, Evaluation and Authorisation of CHemicals

## Slide 4: REACH: KEY ELEMENTS
Introduces a Single Coherent System for new (non phase-in) and existing (phase-in) substances
Key elements:
  Registration by industry of manufactured/imported chemical substances > 1 tonne/year (staggered dead-lines over 11years)
  Increased information and communication throughout the supply chain
  Evaluation of some registered substances (Agency and Member States)
  Authorisation only for use of substances of very high concern
  Restrictions: “Safety net” (Community wide action)
  Chemicals Agency to efficiently manage the system
Focus on priorities:
  High volumes (chemicals with greatest likely exposure register first)
  Greatest concern (CMR and R50/53 register first)
Notes: Evaluation: Testing proposals (animal testing), conform to registration requirements

## Slide 5: Registration: general
AIM:
 Manufacturers and importers obtain information on their substances and
Use this knowledge to ensure responsible and well-informed management of the risks these substances may present
Registration Dossier = Documentation
 Technical Dossier: starting at 1 tonnes per year
 Chemical Safety Report: starting at 10 tonnes per year and if classified as hazardous substance!
No formal acceptance - industry retains responsibility

## Slide 6: Who Has to Register?
Manufacturers and importers.
  DUs may notify non-pre-registered substances of interest
    By doing so DU obliged to submit “light”-registration dossier
Producers of articles (conditions of Article 7).
  Intended release of substances only
Manufactures of substances outside the EU may appoint an “only representative” to fulfil their REACH obligations.
  “Only representative” relieves importers of their duties.
  Importers are then considered DUs.

## Slide 7: REACH
GHS
CLP
INTERCONNECTIONS

## Slide 8: What is CLP?
Regulation (EC) No 1272/2008 of the European Parliament and of the Council of 16 December 2008 on Classification, Labelling and Packing (CLP) of substances and mixtures, amending and repealing Directive 67/548/EEC (i.e.DSD) and 1999/45/EC (i.e DPD) and amending Regulation No 1907/2006 (i.e. REACH) came into force on 20 January 2009
Implements Globally Harmonised System (GHS) of Classification and labelling in the EU
Covers all 27 EU and EEA countries
GHS sets optional building blocks from which countries can choose

## Slide 9
Why do we need GHS?
GHS Danger (Skull & Cross Bones)
Transport liquid: slightly toxic; solid: not classified
EU Harmful (St Andrew’s Cross)
US Toxic
CAN Toxic
Australia Harmful
India Non-toxic
Japan Toxic
Malaysia Harmful
Thailand Harmful
New Zealand Hazardous
China Not Dangerous
Korea Toxic
Substance - oral toxicity LD50 = 257 mg/kg

## Slide 10: CLP & REACH Timelines Compared
Substances
Mixtures
1 June
2007
CLP Regulation
REACH: registration deadlines (substances)
HPV, >1t/a CMRs,
>100t/a R50/53
> 100 t/a
> 1 t/a
CLP compulsory
1 Dec 2010
1 Jun 2015
1 June 2013
1 Jun 2018
20 January 2009

## Slide 11
Obligations - Authorities
The authorities having obligations and rights in
the REACH processes are:
the Agency (specifically set up for REACH) - ECHA,
the Member States Competent Authorities and
the European Commission.
The authorities carry out the evaluation, authorisation and
restriction processes of REACH.
In addition, the Agency and Member States will provide
helpdesk assistance. Member States are responsible for
Enforcement under REACH.

## Slide 12
The Forum for Exchange of Information on Enforcement (Forum), coordinates a
network of Member State enforcement authorities, and has the tasks to:
Spread good practice and highlight problems at Community level
Propose, coordinate and evaluate harmonised enforcement projects and
joint inspections
Coordinate exchange of inspectors
Identify enforcement strategies, as well as best practice in enforcement
Develop working methods and tools of use to local inspectors
Develop an electronic information exchange procedure
Liaise with industry, taking particular account of the specific needs of SMEs,
and other stakeholders, including relevant international organisations, as necessary
Examine proposals for restrictions with a view to advising on enforceability
(Art.77(4))
Agree common issues to be covered in the annual reports from the Member
States in relation to enforcement (Art. 127).
ENFORCEMENT FORUM - ECHA

## Slide 13
Enforcement of REACH and CLP is a national responsibility, therefore
each EU Member State, Norway, Iceland and Liechtenstein must
ensure that there is an official system of controls and lay down legislation
specifying penalties for non-compliance with the provisions of REACH.
The enforcement of the requirements of the REACH and CLP Regulations involves
different enforcement authorities and other bodies. The environmental
inspectorate can play a coordinating role.
There is a need for a national strategy defining the needs for co-operation and
coordination between these enforcement authorities to ensure effective and
efficient enforcement of REACH and CLP.
A key element in any strategy is to define the roles and responsibilities of
the various groups involved. This would allow for an
efficient enforcement process, avoiding gaps and dealing with any overlaps
in the enforcement competencies and responsibilities.
ENFORCEMENT – NATIONAL

## Slide 14
To handle the various requirements under REACH and CLP the training subjects might cover:
Background and basics REACH and CLP;
Roles and responsibilities under REACH;
Enforcement strategies;
Cooperation and coordination between enforcement authorities;
Minimum Criteria for REACH and CLP inspections;
Linkage of REACH and IED;
Downstream consequences of REACH/CLP on other legislation (including SEVESO and Waste).
*Cooperation with the ECHA FORUM is envisaged
TRAINING SUBJECTS*

## Slide 15
Task 1.2.4 Compliance with REACH/CLP Regulations
REACH and CLP are regulations and are therefore directly applicable. As they
enter into force, they will automatically form part of Member States’
national laws. In order to enable REACH and CLP to operate effectively in
practice, Member States are obliged to establish the necessary arrangements
for their implementation
The enforcement of the requirements of the REACH and CLP Regulations involves
different enforcement authorities and other bodies. The environmental
inspectorate can play a coordinating role.
No. | Date | Key outputs
1 | January-February 2015 | Regional Training Workshop 1, methodology, materials and report
2 | October - November 2015 | Regional Training Workshop 2, methodology, materials and report
3 | TBD | National training courses methodology, materials and reports (if requested)

## Slide 16
TASK 5: Transfrontier Shipment of Waste
(TFS)

## Slide 17
RENA ECENA 2010 – 2013
TFS/WSR
Inspection at Ambarli Harbour, Istanbul, Turkey and
cross-border road transport at the border of FYR of
Macedonia and Serbia with IMPEL
Notes: After receiving a gas free certificate the container was opened and the contents showed that the single use camera’s still held the batteries.
17

## Slide 18
The regional trainings delivered on the same subject under RENA has used
the regional road and harbour as selected sites. During identification
of follow up activities, it has been suggested by one of the beneficiary
(Croatia) to organise an inspection for cross border rail transport
(one of the borders of Croatia with neighbouring countries).
Another proposal is to focus on inspection of shipment of waste in ports (maritime area).
In addition to the activities organised within the beneficiary countries,
a 1-day workshop and study visit might be organised in one of the EU member
states for a limited number of participants. The organisation of study visit will
be closely coordinated with IMPEL Cluster 2 TFS.

## Slide 19
Based on the experience gained under the same exercise implemented under RENA,
the attention should be paid to elements such as:
The notification procedures;
Possibilities for upstream enforcement;
The step-by-step-guidance for waste shipment inspections (IMPEL Manual);
Managing illegal shipment of wastes (IMPEL Manual);
Inspection plan and protocol;
Required skills of inspectors;
Sampling plan.
TRAINING SUBJECTS*
* Cooperation with IMPEL is envisaged

## Slide 20
Task 1.2.5 Trans frontier Shipment of Waste (TFS)
To continue the work on what has been accomplished within RENA together
with IMPEL, it is proposed to organise up to 2 regional trainings combined with
a site visit to consolidate and increase the know-how and improve the required
institutional structures. Cooperation with IMPEL is again envisaged
No. | Date | Key outputs
1 | 2,3 July 2014 | Regional Training Workshop 1 (Croatia?), methodology, materials and report
2 | May 2015 | Regional Training Workshop 2, methodology, materials and report
3 | March 2016 | Report on study visit (1) to the selected EU MS Institution