## Slide 1: Country specific topic
Task 2.3.4: WFD and Marine Strategy Framework Directive (MSFD) – where to draw the line?

## Slide 2: Comparison between WFD and MSFD
In the context of setting the Good Environmental Status (GES):
Both directives require ecosystem approach;
Based on adaptive management;
Setting of environmental targets is based on chemical quality and biological status
Changes in the structure and functioning of ecosystems should be addressed.
Identification of coastal water body types as required by Water Framework Directive (WFD) is not required for Marine Strategy Framework Directive (MSFD).
Characterisation of hydro-morphological and physical features is a part of the initial assessment of the MSFD links to WFD typology.
The common coastal types, defined for the WFD intercalibration, are based on the differences in the physical/ freshwater discharge regime in all regional seas. Check alignement with the marine regions and sub-regions identified for the MSFD.
MSFD requires assessment of the marine habitat types (not included in the WFD). Biological quality element specific assessment and classification systems developed for WFD purposes are generally habitat specific. Final classification of WFD should also consider all habitats in a water body.

## Slide 3: Comparison between WFD and MSFD
Reference conditions in the sense of WFD are not required by MSFD.
The spatial approach for the identification of RC for coastal waters was not generally applicable as reference sites are rare in coastal waters.
The setting of GES targets should link to the WFD 'good ecological' status values defined for coastal waters in those areas where the directives overlap and where same indicators may be used in the assessment.
The normative definitions were useful in the process of setting the 'good ecological status' for the WFD, and those were applied as part of the WFD intercalibration process.
Several indices developed for WFD purposes follow the concepts of the normative definitions and can be used to assess the changes in biomass, species composition (sensitive vs. non-sensitive species).
Such community/ habitat specific indices may be applied also to MSFD determination of GES, which would allow application of the conceptual approach of normative definitions in order to facilitate the setting of GES.
Harmonisation and standardisation of sampling, analysis, and assessment tools for chemical and biological parameters will be needed in order to enable comparison and harmonised assessment across the regional sea and sub-regions (and between Member States).
Also there should be an agreement of the indicators that will be applied between sub-regions and regional seas to show distance or progress towards the GES.

## Slide 4: Specific topic candidates
Monitoring, indicators and/or risk assessment issues;
National approaches and outcomes of the initial assessments;
Targets and indicators developed to assess Good Environmental Status (GES);
Approaches to integrate assessments across indicators and descriptors;
Coordination of approaches to implementation across marine regions;
Progress on the development of monitoring programmes to assess GES;
Assessments of the costs and benefits of implementation of the MSFD;
Maintaining the functional integrity of the coastal resource systems;
Reducing resource-use conflicts;
Maintaining the health of the marine environment;
Facilitating the progress of integration among sectors within the coastal/marine environment and realisation of a common goal focused around sustainability.