## Slide 1: Case example: AA for the 2nd Transport Sector Strategy of the Czech Republic for 2014-2050
Zagreb, October 30 – 31, 2014

## Slide 2: 2nd Transport Sector Strategy (2TSS)
Selects priority transport projects for implementation in 2014-2020, 2020-2035 and 2035-2050.
Over 1270 road projects in 260 clusters, 360 rail projects in 90 cluster, and 20 water projects in 3 clusters
Information on current and predicted transport intensities with and without proposed projects in year 2050, locations of all corridors +/- 1 km, iso-lines
Multicriterial analysis
  Needs for the project (economic, transport, etc.)
  Risks that the project faces (formal criteria related to land-use planning and EIA), and
  Preliminary CBA

## Slide 3: SEA
SEA started in Dec 2011, completed in Sept 2013
Based on opinion from Natura 2000 management authorities, AA had to be conducted
Key issues
  Biodiversity and Natura 2000
  Air quality (urban areas, ecosystems)
  Health (air quality, noise, accessibility)
  Other: water, cultural heritage, forests, soil
  Transboundary impacts

## Slide 4: Biodiversity and Natura 2000
Natura 2000
Special protected areas; Habitats of specially protected species of national importance; Areas with occurrence of many specially protected species
Loss of natural habitats
Important landscape feature, Supra-regional and regional territorial systems of ecological stability
Natural parks, Scenic landscapes,
Landscape fragmentation (new projects in unfragmented area by traffic; in areas important for migration)
Water regime of landscape (wetlands, protected areas for natural accumulation of water and large forest areas)

## Slide 5: Approach to AA
Fully integrated in SEA
AA expert addressed also impacts on biodiversity and ecosystems, joint inputs to 2TSS
Specific chapter in SEA report summarizing key findings regarding Natura 2000 + full AA report in the annex
AA focused on relevant parts of the 2TSS
  Principles and objectives
  Measures for transport infrastructure development
  Methodology for project evaluation
  2TSS implementation

## Slide 6: Approach to AA
2TSS is a country-wide strategy, therefore all Natura 2000 sites could be potentially affected (1082+41)

## Slide 7: Approach to AA
2TSS is a country-wide strategy, therefore all Natura 2000 sites could be potentially affected (1082+41)
Scale used for impacts
  -2 Significant negative impact
  -1 Moderate negative impact
  0 ‘Zero’ impact
  +1 Moderate positive impact
  +2 Significant positive impact
  ? Impact cannot be evaluated

## Slide 8: Evaluation of priorities and objectives
Difficult to evaluate, the impacts will depend on the way of implementation
Risks regarding Natura 2000 relate to all objectives, whose implementation requires construction of new transport infrastructure or significant modifications of existing one
However, the likely impacts can be often avoided by routing or technical measures

## Slide 9: Evaluation of specific measures
All clusters evaluated based on
  GIS data (i.e. likely territorial conflicts)
  Information from previous studies (EIA etc.)
  Knowledge of the Natura 2000 sites at risk
Following was determined for each cluster
  Scale of likely impact
  Natura 2000 site(s) likely to be affected
  Verbal description of likely impacts (what exactly can cause impacts, which specific features of the site can be affected)
  Proposed mitigation measures

## Slide 10: Evaluation of specific measures
Significant negative impacts on Natura 2000 sites identified for several clusters
  Roads
  Railroads
  Infrastructure for water transport (locks/chambers, navigation channels)
These clusters were proposed to be removed from 2TSS
After ‘tough fights’ this was accepted by the Ministry

## Slide 11: Conclusions
2TSS will not have significant negative impacts on Natura 2000
However, certain conditions have to be followed
  EIA (including AA) with ‘positive’ statement has to be carried out for water lock on Elbe River
  MCA to be used for project evaluation has to include detailed evaluation of likely impacts on Natura 2000