## Slide 1: Appropriate Assessment and SEA/EIA
Zagreb, October 30 – 31, 2014

## Slide 2: SEA and EIA
Globally recognized as tools for mainstreaming sustainability issues in planning and project permitting
Sustainability issues
  Protection of environmental components (air, soil, water, biodiversity…)
  Environmental management (waste, energy, flood control…)
  Human health (mainly environmental health determinants)
  Social aspects (wellbeing, poverty, (un)employment…)
  Other sectors and approaches (sustainable transport, tourism, integrated coastal management…)

## Slide 3: SEA and EIA
Applied for well-defined group of plans, programmes and projects
  Having likely significant adverse effects on environment and/or human health
  Meeting certain administrative criteria
    Adopted /permitted through formal procedure
    Cover certain area (plans and programmes)
    Creating framework for future projects to be assessed through EIA (plans and programmes)
    Certain types (projects)
    Above certain thresholds (projects)

## Slide 4: SEA and EIA
Conclusions have to be ‘taken into account’ when adopting the plan or programme or issuing project permit
Do not decide about (dis)approval / rejection

## Slide 5: Appropriate Assessment
Applied within EU
Focusing on likely significant impacts on Natura 2000 sites only (i.e., not on national protected areas etc.)
Must address ‘any plan or project’ (no lists)
Conclusions are binding, i.e. AA decides about plan, programme, or project

## Slide 6: Procedural aspects
SEA/EIA usually more structured compared to AA processes
Public does not need to be obligatorily involved in AA
Screening
Scoping
Baseline analysis
Impacts assessment and mitigation measures
SEA/EIA report
QC
Screening
Main assessment
Alternatives
IROPI test and compensatory measures

## Slide 7
Screening
Scoping
Baseline
Impact assessment and mitigation measures
SEA/EIA Report
QC
Consultations
Screening
Main assessment
IROPI and compensatory measures
Alternatives

## Slide 8
SEA/EIA
Global tools
Dealing with limited number of PPP
Address wide range of issues
Deals with significant effects
Process more structured
Public has to be involved
Provide inputs to decision
AA
EU-wide
To be applied for any PPP
Specific focus on Natura sites
Deals with significant effects
Less stages in procedure
Public involved if appropriate
Presents decision itself

## Slide 9: Possible relationship
Separate processes (e.g. UK) x joint procedure (e.g. CR)
Pros and cons
  Joint procedure avoids overlaps in analyses and consultations
  Separate AA may focus only on Natura 2000, however it might lead to certain duplication in analyses (regarding biodiversity and ecosystems)
  Separate AA requires additional formal procedures and thus (together with SEA/EIA) it might take longer time then joint assessment
  Not clear legal power of final statement (if exists) in case of joint procedure

## Slide 10: Case example: AA and SEA/EIA procedure in the Czech Republic
Zagreb, October 30 – 31, 2014

## Slide 11: Procedural steps in SEA/EIA
Notification
Fact-finding procedure (screening + scoping)
SEA/EIA report
Independent expert review (only for EIA)
Public consultations
SEA/EIA statement

## Slide 12
Notification
Screening + Scoping
SEA/EIA Report
Expert review (EIA)
Public consultations
SEA/EIA statement
Opinion regarding AA
Information regarding Natura 2000 and likely impacts
Nature protection authorities can give opinion
Specific chapter regarding likely impacts on Natura 2000
Separate section regarding likely impacts on Natura 2000
Nature protection authorities can give opinion

## Slide 13: SEA/EIA and AA in the Czech Republic
AA is fully integrated in SEA/EIA processes
  0. Planning agency/investor has to get opinion from Natura 2000 managing authorities regarding a need of AA
Screening (and scoping) stage of SEA/EIA
  Opinions of managing authorities are included in the notification
  SEA/EIA competent authority issues screening (and scoping) stipulating a need for SEA/EIA together with requirements for AA
SEA/EIA report
  Includes dedicated chapter on AA with unambiguous conclusion

## Slide 14: SEA/EIA and AA in the Czech Republic
Quality control
  Focused on SEA/EIA report including AA chapter
Consultations
  SEA/EIA report including AA chapter is publicised and is a subject of public hearing
Final statement
  Has two parts 1. SEA/EIA, 2. AA
  If AA is negative, the whole statement is negative i.e. PPP cannot go ahead

## Slide 15: Quality control in SEA/EIA
Internal quality control i.e. done by SEA/EIA team during the process
SEA/EIA-certified or licensed experts and/or companies (both legally required or voluntarily schemes)
Quality control by SEA/EIA Competent authorities is usually conducted on the SEA/EIA Report submitted before further public consultations
Expert(s) appointed to review the quality of SEA/EIA report and prepare the quality review report
Ad-hoc committees (more usual in EIA) established specifically for each SEA or EIA process and often focusing on the SEA/EIA report only
Specialized institutions conducting the quality control of SEA/EIA report
Provisions for checking agreed mitigation measures are implemented and effective
Public scrutiny can be considered as one of the most strict

## Slide 16: Quality control in AA
Internal quality control i.e. done by the AA experts during the process
By nature protection authorities (as a part of SEA/EIA QC)
Expert(s) appointed to review the quality of SEA/EIA report and prepare the quality review report addressing also AA part
Provisions for checking agreed compensatory measures are implemented and effective
Public scrutiny

## Slide 17
Thank you for your attention!