## Slide 1: GHG emission calculation and reporting obligations of TPP Plomin under national regulation
Ivana Laković,dipl.ing
HEP Proizvodnja d.o.o TE Plomin

## Slide 2: Reporting obligation under Croatian national regulation
GHG Emission:
31.03.2014. :
- The Verifier must finish the verification and issue verification report to the
operater
Operator must submitt verified annual emission report
30.04.2014. :
- Operator must surrender allowances (amount corresponding to verified
annual emissions) in Registry system
REGISTRY OF ENVIROMENTAL POLUTION (ROO):
1.03.2014. :
The operater must fill the registry with data: emissions in water,air,land and amount of wast produced in the past year (2013.)
Until 01.01.2013. - CO2 emissions(data from the Registry)/tone x 18 kn → payed to Fond for enviromental protection and energy efficiency
From 01.01.2013. part of EU ETS

## Slide 3: TPP Plomin
TPP Plomin 1
(1970.)
339 MWth
CO2 emission from combustion:
COAL (≈350 000t/y →780000 t CO2)
LIGHT OIL DESTILATE (≈150t/y→450t CO2)
DIESEL OIL (≈0,2 t/y→0,8t CO2)
TPP Plomin 2
(2000.)
556MWth
CO2 emission from combustion:
COAL (≈600 000t/y→1 389 000t CO2)
LIGHT OIL DESTILATE(≈500t/y→1460t CO2)
DIESEL OIL (≈0,2 t/y→0,9t CO2)
CO2 emission – process emission:
LIMESTONE (≈15000t/y→6470t CO2)
USA
Columbija
Russia
FGD
780 450 t CO2
1 396 930t CO2
2 177 380 t CO2
TOTAL

## Slide 4
COAL
BOILER
TEP 2
B EAC 61CW002
M1
LOD
SMALL BOILER - PK2
Fuel tanks
Bill of lading
Draft broda
Coal analysis
Bill of lading
M2
CO2 BORDERS
SOURCES OF EMISSION
Limestone
TEP 1
TEP 1
Other buyers
Diesel aggregat DA 2
FGD
Diesel
oil
Conveyor belt scale
TPP Plomin 2

## Slide 5: GHG MONITORING PLAN FOR TPP PLOMIN 2
Categorisation of installation, emission sources and source streams
Instalation categorisation:
TP Plomin 2 → Category C: Annual average emissions are more than 500 000 tonnes of CO2
Source streams :
major source – Coal, around 1400 000 t/y CO2
de-minimis source streams (less than 1 000 tonnes of fossil CO2 per year or to
less than 2% of the “total of all monitored items”, up to a total maximum contribution
of 20 000 tonnes of fossil CO2 per year) – emissions from Liquid fuels( light oil destilate, diesel oil)
and Limestone
Monitoring approach
Calculation based approach
The tier system
Each parameter needed for the determination of emissions
can be determined by different “data quality levels”.
These “data quality levels” are called “tiers”
Uncertainty

## Slide 6
Caregory C; solid fuel | Tier required | Tier achieved |  | Uncertainty required /achieved
COAL |  |  |  | 
Consumption of fuel | 4 | 4 | Conveyor belt scale | ±1,5%/±1,5%
Net Calorific value | 3 | 3 | Laboratory analysis (every 20 000t) | 
Emmision factor | 3 | 3 | Laboratory analysis(every 20 000t) | 
Oxidation factor | 1 | 1 | 1,0 | 
LIGHT OIL DESTILATE – de minimis source |  |  |  | 
Consumption of fuel | 1 | 1 | Bill for lading | bill
Net Calorific value | 1 | 2a | Default values/NIR 2013 | 42,71
Emmision factor | 1 | 2a | Default values/NIR 2013 | 74,07
Oxidation factor | 1 | 1 | 1,0 | 
Diesel Oil –de minimis source |  |  |  | 
Consumption of fuel | 1 | 1 | Estimation | 
Net Calorific value | 1 | 2a | Default values/NIR 2013 | 42,71
Emmision factor | 1 | 2a | Default values/NIR 2013 | 74,07
Oxidation factor | 1 | 1 | 1,0 | 
Limestone - de minimis source |  |  |  | 
Consumption of fuel | 1 | 1 | Bill for lading | bill
Emmision factor | 1 | 1 | Default values | 
Emission sources -Tiers - Uncertainty Tabel
Measuring instrument must achieve the required uncertainty

## Slide 7: Monitoring approach - Calculation based approach
1.CO2 emission from Coal:
CO2 (COAL) = consumption (t) x NCV (TJ/t) x EF (tCO2/TJ) x OF
For all types of coal in one year fron 1 to n
2.CO2 emission from Light oil and Diesel oil:
CO2 (LO) = consumption (t) x NCV(TJ/t) x EF (tCO2/TJ) x OF
CO2 (D) = consumption (t) x NCV(TJ/t) x EF (tCO2/TJ) x OF
NVC = 42,71 TJ/Gg EF = 74,07 tCO2/TJ

## Slide 8
3.CO2 emission from Limestone:
CO2 (Limestone) = consumption (t) x EF (tCO2/tCaCO3)
= consumption (t) x 0,44
TOTAL CO2 emission :
CO2 (All fuels) = CO2 (COAL) +CO2 (LOD)+CO2(DO)+CO2(Limestone)

## Slide 9: Uncertainty for calculation-based approaches
Only one measuring instrument must acchieve required uncertainy :
CONVEYOR BELT SCALE
Consumption of coal → Conveyor belt scale → Tier 4→ Uncertainty= ±1,5%
In our case ROUTE CO- 2b
Uncertainty =
Uncertaintycalibration
X
Conservative Adjustment Factor
Uncertaintycalib. = ± 0,75 %
Conservative Adjustment Factor = 2
Uncertainty= 0,75 x 2= ±1,5 %

## Slide 10
THANK YOU !