## Slide 1: Case example – Scoping: SEA for the 2nd Transport Sector Strategy of the Czech Republic for 2014-2050
Podgorica, September 23 – 26, 2014

## Slide 2: 2nd Transport Sector Strategy (2TSS)
Selects priority transport projects for implementation in 2014-2020, 2020-2035 and 2035-2050.
Over 1270 road projects in 260 clusters, 360 rail projects in 90 cluster, and 20 water projects in 3 clusters
Information on current and predicted transport intensities with and without proposed projects in year 2050, locations of all corridors +/- 1 km, iso-lines
Multicriterial analysis
  Needs for the project (economic, transport, etc.)
  Risks that the project faces (formal criteria related to land-use planning and EIA), and
  Preliminary CBA

## Slide 3: SEA
SEA started in Dec 2011, completed in Sept 2013
3 core members of the SEA team, 3 experts for air, biodiversity, N2K, health, 1 short term terms for other topics
EUR 23,000
Key issues
  Biodiversity and Natura 2000
  Air quality (urban areas, ecosystems)
  Health (air quality, noise, accessibility)
  Other: water, cultural heritage, forests, soil
  Transboundary impacts

## Slide 4: Biodiversity and Natura 2000
Natura 2000
Special protected areas; Habitats of specially protected species of national importance; Areas with occurrence of many specially protected species
Loss of natural habitats
Important landscape feature, Supra-regional and regional territorial systems of ecological stability
Natural parks, Scenic landscapes,
Landscape fragmentation (new projects in unfragmented area by traffic; in areas important for migration)
Water regime of landscape (wetlands, protected areas for natural accumulation of water and large forest areas)

## Slide 5: Air
Changes of transport intensities in:
Urban areas (old and new roads, increasing and reducing intensities bellow 15,000 cars per day)
Sensitive ecosystems (large-scale protected areas, forests, areas above 800 m)
Total emissions in areas with poor air quality status

## Slide 6: Human health
Air emissions in urban areas
Noise (isolines 60 dB)
Socio-economic impacts (accessibility for work-related travel and social and health services)

## Slide 7: Other minor issues
Water: areas of natural water accumulation and water bodies for drinking water supply, protected areas of mineral waters, barrier effect in flood zones)
Soil: general impacts on soil types
Cultural heritage (nationally important cultural monuments and heritage reserves - impacts caused by noise, vibration and aesthetic concerns)
Climate change: consistency with relevant targets for climate change mitigation in the transport sector

## Slide 8: Issues scoped out
Waste
Soil and forests – SEA team proposed to scope these out, however MoE required “full scope of assessment”