## Slide 1: Case example – Impacts analysis: SEA for Krasna Hora municipal spatial plan
Podgorica, September 23 – 26, 2014

## Slide 4: Main features of spatial plan
Amendments of existing plan
  Aim is to “examine and modify current functions of certain localities and to identify new areas for urbanization”
  Purpose is to “define new localities for building, for additional service functions in municipality, and other areas for small businesses and manufactures, which will provide new working places in the area. Important is also recreational function”.
  Altogether 11 localities proposed to be modified (i.e. to change their function)

## Slide 5
Landscape | Likely adverse impact (less significant, direct, permanent); location close to inhabited area can cause local change of the landscape character, area use shall not include large buildings.
Soil | Likely adverse impact (less significant, direct, permanent); change will cause degradation of agriculture land (total area 2,11 ha), it can also cause soil pollution.
Public health | Likely adverse impact (secondary, short-term, temporary); change can cause higher emissions to the air and noise from manufacture and traffic. Since location neighbours with houses, its necessary to minimize these impacts (to move facility further from houses, find better transport connection, to implement “green belt”). Specific impact to the public health depend on the specific type of manufacture, and have to be addressed in detail within further procedures (building permits and EIA).

## Slide 6: Proposed mitigation
To exclude of 1 location from the plan
To modify 3 locations (area reduction, different land-use)
To modify some project proposed for implementation on selected locations
+ conditions for implementation

## Slide 7: Conditions for implementation
Due to close location to inhabited area, its necessary to conduct detail noise and emission study before the project implementation. Study has to include also assessment of potential cumulative impacts with already existing agriculture production.
The most noisy parts of the manufacture place as far from the inhabited area as possible
The separate family houses from the manufacture by “green belt”
To save trees along the road
To solve waste water and rain water management before initiation of development of the area